## Slide 1: An opportunistic HTCondor pool inside an interactive-friendly Kubernetes cluster
At HTCondor Week 2019
Presented by Igor Sfiligoi, UCSD for the PRP team

## Slide 2: Outline
Where do I come from?
What we did?
How is it working?
Looking head

## Slide 3: The Pacific Research Platform
The PRP originally created as a regional networking project
  Establishing end-to-end links between 10Gbps and 100Gbps
(GDC)

## Slide 4: The Pacific Research Platform
The PRP originally created as a regional networking project
  Establishing end-to-end links between 10Gbps and 100Gbps
Expanded nationally since
  And beyond, too

## Slide 5: The Pacific Research Platform
Recently the PRP evolved in a major resource provider, too
  Because scientists really need more than bandwidth tests
  They need to share their data at high speed and compute on it, too
The PRP now also provides
  Extensive compute power – About 330 GPUs and 3.5k CPU cores
  A large distributed storage area - About 2 PBytes
Select user communities now directly use all the resources PRP has to offer
  Still doing all the network R&D in the same setup, too
  We call it the Nautilus cluster

## Slide 6: Kubernetes as a resource manager
Industry standard
Large and active development and support community
Container based
More freedom for users
Flexible scheduling
Allows for easy mixing of service and user workloads

## Slide 7: Designed for interactive use
Users expect to get what they need when they need it
Makes for very happy users
Congestion happens only very rarely
And is typically short in duration

## Slide 8: Opportunistic use
No congestion
Idle compute resources
Time for opportunistic use

## Slide 9: Kubernetes priorities
Priorities natively supported in Kubernetes
Low priority pods only start if no demand from higher priority ones
Preemption out of the box
Low priority pods killed the moment a high priority pod needs the resources
Perfect for opportunistic use
Just keep enough low-priority pods in the system
https://kubernetes.io/docs/concepts/configuration/pod-priority-preemption/

## Slide 10: HTCondor as the OSG helper
PRP wanted to give opportunistic resources to Open Science Grid (OSG) users
Since they can tolerate preemption
But OSG does not have native support for Kubernetes
Supports only resources provided by batch systems
We thus instantiated an HTCondor pool
As a fully Kubernetes/Containerized deployment

## Slide 11: HTCondor in a (set of) container(s)
Putting HTCondor in a set of containers is not hard
Just create an image with HTCondor binaries in it!
Configuration injected through Kubernetes pod config
HTCondor deals nicely with ephemeral IPs
Everything else just works from there
Persistency needed for the Schedd(s)
And potentially for the Negotiator, if long term accounting desired
Everything else can live off ephemeral storage
The Collector must be discoverable – Kubernetes service

## Slide 12: Service vs Opportunistic
Collector and Schedd(s) deployed as high priority service pods
Should be running at all times
Few pods, not high CPU or GPU users, so OK
Using Kubernetes Deployment to re-start the pods in case of HW problems and/or maintenance
Kubernetes Service used to get a persistent routing IP to the collector pod
Startds deployed as low priority pods
Hundreds of pods in the Kubernetes queue at all times, many in Pending state
HTCondor Startd configured to accept jobs as soon as it starts and forever after
If pod preempted, HTCondor gets a SIGTERM and has a few seconds to go away
Pure opportunistic

## Slide 13: Then came the users
Everything was working nicely, until we let in real users
Well, until we had more than a single user
OSG users got used to rely on Containers
So they can use any weird software they like
But HTCondor Startd already running inside a container!
Cannot launch a user-provided container
So I need to provide user-specific execute pods
How many of each kind?
Not without elevated privileges

## Slide 14: Then came the users
Everything was working nicely, until we let in real users
Well, until we had more than a single user
OSG users got used to rely on Containers
So they can use any weird software they like
But HTCondor Startd already running inside a container!
Cannot launch a user-provided container
So I need to provide user-specific execute pods
How many of each kind?

## Slide 15: Dealing with many opportunistic pod types
Having idle Startd pods not OK anymore
A different kind of pod could use that resource
A glidein-like setup would solve that
Keeping pods without users not OK anymore
They will just terminate without ever running a job
Who should regulate the “glidein pressure”?
How do I manage fair share between different pod types?
Kubernetes scheduling is basically just priority-FIFO
How am I to know what Container images users want?
Ideally, HTCondor should have native Kubernetes support

## Slide 16: Dealing with many opportunistic pod types
Having idle Startd pods not OK anymore
A different kind of pod could use that resource
A glidein-like setup would solve that
Keeping pods without users not OK anymore
They will just terminate without ever running a job
Who should regulate the “glidein pressure”?
How do I manage fair share between different pod types?
Kubernetes scheduling is basically just priority-FIFO
How am I to know what Container images users want?
Ideally, HTCondor should have native Kubernetes support
I know how to implement this.

## Slide 17: Dealing with many opportunistic pod types
Having idle Startd pods not OK anymore
A different kind of pod could use that resource
A glidein-like setup would solve that
Keeping pods without users not OK anymore
They will just terminate without ever running a job
Who should regulate the “glidein pressure”?
How do I manage fair share between different pod types?
Kubernetes scheduling is basically just priority-FIFO
How am I to know what Container images users want?
Ideally, HTCondor should have native Kubernetes support
I was told this is coming.

## Slide 18: Dealing with many opportunistic pod types
Having idle Startd pods not OK anymore
A different kind of pod could use that resource
A glidein-like setup would solve that
Keeping pods without users not OK anymore
They will just terminate without ever running a job
Who should regulate the “glidein pressure”?
How do I manage fair share between different pod types?
Kubernetes scheduling is basically just priority-FIFO
How am I to know what Container images users want?
Ideally, HTCondor should have native Kubernetes support
In OSG-land, glideinWMS solves this for me.

## Slide 19: Dealing with many opportunistic pod types
Having idle Startd pods not OK anymore
A different kind of pod could use that resource
A glidein-like setup would solve that
Keeping pods without users not OK anymore
They will just terminate without ever running a job
Who should regulate the “glidein pressure”?
How do I manage fair share between different pod types?
Kubernetes scheduling is basically just priority-FIFO
How am I to know what Container images users want?
Ideally, HTCondor should have native Kubernetes support
No concrete plans on how to address these yet.

## Slide 20: Dealing with many opportunistic pod types
For now, I just periodically adjust the balance
A completely manual process
Currently supporting only a few, well behaved users
Maybe not optimal, but good enough
But looking forward to a more automated future

## Slide 21: Are side-containers an option?
Ideally, I do want to use user-provided, per-job Containers
Running HTCondor and user jobs in separate pods not an option due to opportunistic nature
But Kubernetes pods are made of several Containers
Could I run HTCondor in a dedicated Container?
Then start the user pod in a side-container?
Pretty sure currently not supported
But, at least in principle, fits the architecture
Would also need HTCondor native support
Pod
HTCondor container
User job container

## Slide 22: Will nested Containers be a reality soon?
It has been pointed out to me that latest CentOS supports unprivileged Singularity
Have not tied it out
Probably I should
Cannot currently assume all of my nodes have a recent-enough kernel
But eventually will get there

## Slide 23: Looking ahead
Looking forward to a more automated future
Will do what I have to myself
Would be happier if I could use off-the-shelf solutions

## Slide 24: A final picture
Opportunistic GPU usage over the past few months

## Slide 25: Summary
We created an opportunistic HTCondor pool in the PRP Kubernetes cluster
  OSG users can now use any otherwise-unused cycles
The lack of nested containerization forces us to have multiple execute pod types
Some micromanagement currently needed, hoping for more automation in the future

## Slide 26: Acknowledgents
This work was partially funded by US National Science Foundation (NSF) awards CNS-1456638, CNS-1730158, ACI-1540112, ACI-1541349, OAC-1826967, OAC 1450871, OAC-1659169 and OAC-1841530.