## Slide 1: Improving the quality of my research on urban residential hydrology by increasing the quantity of simulations using HTCondor
HTCondor Week, May 22, 2019
Carolyn Voter, University of Wisconsin-Madison
cvoter@wisc.edu carolynbvoter.weebly.com @VoteWater

## Slide 2: Urbanization messes with how water flows
Evapotranspiration
Runoff
Infiltration
Runoff
Infiltration
Evapotranspiration
Rain
Rain
NATURAL
URBAN

## Slide 3: Urbanization messes with how water flows
Today’s Approach
Last Millennium's Approach

## Slide 4: Homeowner decisions affect urban hydrology
Soil Condition
vs.
Downspout
Sidewalk
Driveway
Microtopography

## Slide 5: Homeowner decisions affect urban hydrology
How do these practices interact with one another?

## Slide 6: Homeowner decisions affect urban hydrology
How do these practices interact with climate?

## Slide 7: Homeowner decisions affect urban hydrology
How do these practices interact with climate?

## Slide 8: Homeowner decisions affect urban hydrology
How do your actions combine with your neighbors’ actions to impact larger scale hydrology?

## Slide 9: Basic Lot Layout
Sidewalk
Front Walk
Driveway
Garage
House
Driveway
Front Walk
= 0.5m x 0.5m grid cell
(to scale)

## Slide 10: Why these models take forever*
Image:
Staudinger et al., 2019 https://doi.org/10.1016/j.jhydrol.2019.01.058
time
*To me

## Slide 11: Why these models take forever*
Image: parflow.org
*To me

## Slide 12: Why I started on HTC
Model too big for desktop  HPC
Postprocessing too small for HPC  Postprocess on HTC
Do everything on HTC!

## Slide 13: HTCondor Workflow
fluxC
out01
out02
out03
out04
fluxA
fluxB
fluxC
fluxD
input
convertInputs.sub
*.sh, *.tcl
runParflow.sub
*.sh, *.tcl
convertOutputs.sub
*.sh, *.mat
calculateOutputs
*.sh, *.mat
4
5
9
13
17
1
2
3
8
6
7
12
10
11
16
14
15
20
18
19
DAGman
SPLICE DAGman files
rearrangeOutputs.sub
*.sh
out01
out02
out03
out04
submit server
gluster file server
compute resources
input
input
fluxA
fluxB
fluxA
fluxC
fluxB
fluxA
fluxB
input
1
2
3
4
5
9
13
17
1
2
3
8
6
7
12
10
11
16
14
15
20
18
19
convertInputs.sub
*.sh, *.tcl
runParflow.sub
*.sh, *.tcl
convertOutputs.sub
*.sh, *.m
calculateOutputs
*.sh, *.m
rearrangeOutputs.sub
*.sh
6-10 models running at any given time
Nearly all take >3 days
Use “+is_resumable”
Send outputs back regularly
Outputs saved by (model) time, I need to process them by hydrologic flux
Inputs need to be converted to parflow binary format and repackaged
Convert to Matlab files for analysis
Derive additional fluxes of interest, check water (mass) balance

## Slide 14: Key wins along the way
Figuring out what “compiling” means
Using DAG and ultimately DAG splice
Sending back output regularly, but not too frequently
Custom script to extract current status of all models

## Slide 15: Current Pinch Points
Limited to Gluster machines
So much data, no (cheap) place for it to go
As my models get bigger, back to hybrid HPC/HTC workflow

## Slide 16: Quantity = Quality
7 scenarios
x 20 processors each
x 5-ish days each
More resources + time than I ever imagined spending on hydrologic modeling
1

## Slide 17: Quantity = Quality
Baseline
Lowest-Impact
Baseline Compaction = ?
1
Notes: But between these two extremes, there are a lot of possible combinations of interventions. So I run all those too. With each model scenario, I’m going to compare the growing season deep drainage to that from the baseline. So I’ll be looking at how much deep drainage changes and comparing those differences.

## Slide 18: Quantity = Quality
Baseline
Lowest-Impact
Baseline
Lowest-Impact
Baseline
Lowest-Impact
Ksat ↓ 10x
Highly Compacted
Ksat ↓ 2x
Moderately Compacted
Weather?
1
Notes: One thing that kind of bothered me about the baseline scenario is this concept of compacted soil. There are a few studies out there that have looked at urban soil hydraulic characteristics and tried to quantify how they are affected by compaction, but there’s a fairly wide range of what they find. So I decided to test 2 different baseline conditions. One where the soil “highly-compacted” and saturated hydraulic conductivity is reduced by a factor of 10, and the other where it’s only moderately compacted and Ksat is reduced by a factor of 2.

## Slide 19: Quantity = Quality
Average
Baseline
Lowest-Impact
Baseline
Lowest-Impact
Ksat ↓ 10x
Highly Compacted
Ksat ↓ 2x
Moderately Compacted
1
Notes: Another thing that kind of bothered me was just running this for “average” growing season in Madison, because conceptually, I can imagine a lot of interesting trade-offs might happen between deep drainage and ET under drier conditions. So I ran these for both an average and a dry year.

## Slide 20: Quantity = Quality
Dry
Baseline
Lowest-Impact
Baseline
Lowest-Impact
Ksat ↓ 10x
Highly Compacted
Ksat ↓ 2x
Moderately Compacted
1

## Slide 21: Quantity = Quality
Ksat ↓ 10x
Highly Compacted
Ksat ↓ 2x
Moderately Compacted
96 simulations
1
Notes: Another thing that kind of bothered me was just running this for “average” growing season in Madison, because conceptually, I can imagine a lot of interesting trade-offs might happen between deep drainage and ET under drier conditions. So I ran these for both an average and a dry year.

## Slide 22: Quantity = Quality
2
WET
DRY

## Slide 23: Quantity = Quality
X
50 Largest U.S. Cities (plus Madison)
Baseline
Low-Impact
humid
arid
2 Lot Types
Hourly weather data WY2014
ET0:P
102 simulations
2

## Slide 24: Quantity = Quality
Reduction in runoff
Estimates for WY1981 – WY2010
2

## Slide 25: Quantity = Quality
3
Compaction ?

## Slide 26: Overland Flow on Compacted Soil

## Slide 27: Quantity = Quality
Top Ranked Pixel
(0.04% of yard)
3

## Slide 28: Quantity = Quality
= Amended pixels
3

## Slide 29: Quantity = Quality
= Amended pixels
3

## Slide 30: Quantity = Quality
All
Amended Features
3
18 simulations

## Slide 31: Thank You!
Questions?
Funding
UW Water Resources Institute, WR12R002
UW Sea Grant Institute, RCE-05
LTER-NTL
Others
Hydroecology Lab
UW Center for High Throughput Computing
Carolyn Voter, Ph.D. Candidate, Civil & Environmental Engineering, UW-Madison
cvoter@wisc.edu carolynbvoter.weebly.com @VoteWater