## Slide 1: A Self-Stabilizing Metasurface Laser Sail To Explore The Stars
Joel Siegel
University of Wisconsin Madison
Physics Department
5/22/19

## Slide 2: Laser Propelled Spacecraft
Starshot Breakthrough Initiative
Laser Sail
High-Power Laser
~10 g,
4x4 m2
~100 GW
Traveling at 1/5th speed of light
Goal is to travel to Alpha Centauri
(~5 light years away)
But how do we keep the sail in the beam?
Notes: Picture of laser sail. *click* There is the laser sail. *click* There is the high power laser. Spacecraft is propelled by momentum transfer of incident photons from a high-power laser
*click* metasurfaces are a suggestion for these sails, but what are the optical forces like? *click* Big finish, can we use the forces to stabilize the sail?

## Slide 3: How fast is 1/5th the speed of light?
747
SR-71 Blackbird
New Horizons
(550mph)
(2,700 mph)
(36,000 mph)
New Horizons
(36,000mph)
(177,000 mph)
(2,365,000 mph)
65xNew Horizons
65xNew Horizons
(2,365,000mph)
(11,570,000 mph / 0.017c)
(152,000,000 mph / 0.2c)
Laser Sail
65xNew Horizons
Gif from Clay Bavor
Took the first close up pictures of Pluto in 2015
One of the fastest man made objects

## Slide 4: Optical Forces
Force
Laser Sail
Force is determined by the reflected/refracted light
If we control how the light reflects/refracts, we can control the optical forces
Force
Notes: Now what I am going to talk about is the reflecting/refracting light imparting a force *click*. By conservation of momentum, there is a force on the metasurface. *click*, text appears.

## Slide 5: Metasurface Based Laser Sail
Thin, lightweight structure with subwavelength scattering elements
Controls the phase and magnitude of reflected/refracted light
n
Prism Beam Steering
Metasurface Beam Steering
~cm
~μm
D. Fattal, et. al., Nature Photonics 4, 466 (2010).
Reflective Metasurface Focusing Lens
Y. Yang, et. al. Nanoletters 14, 1394 (2014).
Optical Vortex Beam Creation
Arbitrary wave-fronts can be generated with a metasurface
Notes: Can be highly reflective. Here we have a metasurface that is highly reflective and it focuses.
What is a Metasurface? Give definition. What makes it different than other optics? Well, consider a prism. Diffracts light. But it is thick. On the other hand, a Metasurface can do the same thing, but it is much thinner.

## Slide 6: Metasurface Example
Gaussian Beam
Forces
Example Metasurface
0
1
Intensity
Notes: Let’s imagine a metasurface. *click* Left side reflects to the right, *click* Details. *click* right side reflects to the left. *click* More details, note that it is basically opposite structure. *click* Let’s have a Gaussian Beam incident on the surface

## Slide 7: Metasurface Motion
Gaussian Beam
Example Metasurface
Offset the Metasurface
Moves back, but also rotates
Metasurface flies away
Motion can be described by:
Rotation
Offset
Dynamic Force Coefficients
How can we control these coefficients to make a metasurface that is stable?
Each metasurface/beam combination has different coefficients
Notes: Let’s imagine a metasurface. *click* Left side reflects to the right, *click* Details. *click* right side reflects to the left. *click* More details, note that it is basically opposite structure. *click* Let’s have a Gaussian Beam incident on the surface

## Slide 8: Designing a Stable Sail
Requires many (>1 Million) computations with slight parameter variations
  Human intuition for the sail designs
Computation Requirements
  1 CPU
  1MB of RAM
  3 GB of Disk
Output of single file is ~10 bytes (0/1 for success/failure and an ID)
Find a set of stable parameters
Create idealized sail to generate those coefficients
Simulate that sail using realistic components
Requires 1 large computation
  Sail design chose from previous stage
Computation Requirements
  80 CPUs
  500 GB of RAM
  5 GB of Disk
Output is ~5 GB
Over 1 million output files! Had to write a shell script to “cat” them all together in pieces
Needed HPC to run– which introduced me to HTC
Noise Applied to Beam
Failure Rate
1 Million CPU hours to produce this plot
Sail to simulate with realistic components

## Slide 9: Idealized Metasurface to Generate Stable Coefficients
Two Offset Gaussians
Metasurface
Highly Reflective, Normal
Partially Transmissive, Parabolic
Inverted Cat Eye (ICE) Metasurface
Notes: Let’s look at a more complex metasurface behaviors. First we have the beam. Two offset gaussians

## Slide 10: Full-Wave Simulation
Steering the Beam
Resonators
Reflected Beam front
Transmitted Beam front
Highly Reflective, Normal
Partially Transmissive, Parabolic
Simulated ICE Metasurface
504 μm, 420 Resonators

## Slide 11: Local Optical Forces on Metasurface
Full-Wave
Ideal
Full-Wave
Ideal
Overall good agreement
Full-Wave
Ideal
Full-Wave
Ideal
Forces calculated at each point on sail
No Offset
No Offset
Offset
Offset
Full-Wave Sail is Stable!
Notes: By offsetting the sail, we can determine the dynamic force coefficients.
We can extract the force coefficients this way and show plot of the motion that is stable. Have the plot overtop.

## Slide 12: What’s next?
Incorporate optimization techniques that can take advantage of throughput computing to more efficiently explore the parameter space
Generate a sail based on a set of dynamic force coefficients without human intuition
Improve the efficiency of our realistic sails by using optimization based metastructures
Figure courtesy of Greg Holdman

## Slide 13: Acknowledgments
Collaborators
Mikhail A. Kats –UW Madison
Sergey Menabde –KAIST
Min Seok Jang –KAIST
Big Thank You to Christina Koch and Lauren Michael for helping me learn to use CHTC
Brar Group