## Slide 1: High-performance multilayer optical haloscope for a dark photon search
Presenter: Jeff Chiles, NIST
Teams/Affiliations:
NIST: Jeff Chiles, Sae Woo Nam, Varun E. Verma, Adriana Lita
MIT: Ilya Charaev, Karl K. Berggren, Marco Colangelo
Perimeter Institute for Theoretical Physics: Asimina Arvanitaki, Junwu Huang
New York University: Masha Baryakhtar
UCSB: Ken Van Tillburg
Stanford: Robert Lasenby

## Slide 2: Intro: detecting dark photons and axions

## Slide 3: The quest for dark matter
Surrounds most if not all galaxies in a halo
Has mass, mostly interacts through gravity
https://www.eso.org/public/videos/eso1217a/
Dark matter halo of milky way
(artist rend.)
95% of galaxy is dark matter
Solar flux ~ 1.4 kW/m2
DM flux ~ 14 W/m2

## Slide 4: Seeing light bosonic dark matter
Photon can convert into axion (dark photon) and back through E·B (kinetic mixing) term

## Slide 5: Seeing light bosonic dark matter
Photon can convert into axion (dark photon) and back through E·B (kinetic mixing) term
Could we see axion or dark photon dark matter converting to photons?
  In theory yes
  Then why don’t we see it all the time?

## Slide 6: Seeing light bosonic dark matter
photon
dark matter
For a given particle energy, oscillation is matched in time
Photon
Dark matter
t

## Slide 7: Seeing light bosonic dark matter
photon
dark matter
But highly spatially mismatched due to dark matter’s mass and slow velocity
Photon
Dark matter
x

## Slide 8: Seeing light bosonic dark matter
A periodic index of refraction can correct the momentum mismatch
Electric field no longer integrates to zero against a constant DM background
t
x
Higher refractive index
M. Baryakhtar et al., Phys. Rev. D 98, 035006 (2018)

## Slide 9: Multilayer haloscope concept
thickness N (d1+d2)
mirror
photodetector
lens
area A ~ (10 cm)2
d1, n1
d2, n2
High index of refraction contrast increases power
  e.g. silicon (n2=3.4) and silica (n1=1.46)
Large number of layers N increases power while decreasing mass coverage
  E&M fields add coherently
Signal photons efficiently focused onto detector
  106 smaller than the stack
M. Baryakhtar et al., Phys. Rev. D 98, 035006 (2018)

## Slide 10: Multilayer optical haloscope design
3 major aspects

## Slide 11: Multilayer optical haloscope design
3 major aspects
  Detector
    -Pick up the signal with low noise
    -Provide large area to ease alignment
(1)

## Slide 12: Multilayer optical haloscope design
3 major aspects
  Detector
    -Pick up the signal with low noise
    -Provide large area to ease alignment
  Multilayer target
    -Convert DM to SM photons
    -Precisely engineered thin film coating for target wavelength
(1)
(2)

## Slide 13: Multilayer optical haloscope design
3 major aspects
  Detector
    -Pick up the signal with low noise
    -Provide large area to ease alignment
  Multilayer target
    -Convert DM to SM photons
    -Precisely engineered thin film coating for target wavelength
  Optomechanical assembly
    -Align all elements (lens, target, detector)
(1)
(2)
(3)

## Slide 14: Superconducting nanowire single photon detectors (SNSPDs)

## Slide 15
Meandered wire of superconducting thin film with a small bias current
Superconducting Nanowire Single-Photon Detector
V. Verma (NIST)
Notes: First, some quick background and theory, for anyone in the audience who is not very familiar with these devices. A modern SNSPD may look something like the device pictured below, a meandered wire of a thin superconducting film. It is cooled well below the superconducting transition temperature and biased with a DC current.

## Slide 16
Superconducting
Photon creates hotspot
IB
RL
L
SNSPD
Suppressed Superconductivity
Superconducting Nanowire Single-Photon Detector
Bias Current (IB)
Anomalously, large Inductance, L
Notes: Zooming in on a small section of the wire – when a photon is incident on it and strikes the surface, it is absorbed by the metallic film and locally changes the critical current, or maximum current density that is permitted before superconductivity breaks down

## Slide 17
IB
RL
L
SNSPD
Superconducting Nanowire Single-Photon Detector
Bias Current (IB)
Normal
Notes: The hotspot becomes normal, or resistive, quickly crowding out an blocking any superconducting path through the wire. As a result, current is diverted into the amplifier monitoring the device, generating a voltage spike that is easily detected.

## Slide 18
Superconducting
IB
RL
L
SNSPD
Superconducting Nanowire Single-Photon Detector
Bias Current (IB)
Anomalously, large Inductance, L
Superconductivity is restored
Notes: After some time, with the bias current removed from the nanowire, it cools down below the transition temperature, at which point it will become a short circuit again.

## Slide 19
Superconducting
Bias Current Restored
IB
RL
L
SNSPD
Superconducting Nanowire Single-Photon Detector
Bias Current (IB)
τ = L / RL
Notes: The bias current settles at the normal value, and the detector is ready for the next photon.

## Slide 20: Detector for optical haloscope
See Ilya Charaev’s talk at 9:35 AM
400 x 400 um2 detectors with 10-5 Hz dark count rate
Notes: For our optical haloscope detector, we used a tungsten silicide thin film deposited at NIST, and Ilya Charaev at MIT, from Karl Berggren’s group, fabricated nanowire detectors on these films. These are some of the largest nanowire detectors to date. For our experiment, we utilized one of his large-area detectors spanning 400x400um^2.

## Slide 21
Large detector areas: increase target size, ease alignment
  Narrow nanowires harder to yield over large surface areas of mm2
  Korneeva et al. recently demonstrated single-photon sensitivity in nanowires > 1 um in width (EPJ Web Conf. 190 (2018))
Scaling up with “microwires”

## Slide 22
Large detector areas: increase target size, ease alignment
  Narrow nanowires harder to yield over large surface areas of mm2
  Korneeva et al. recently demonstrated single-photon sensitivity in nanowires > 1 um in width (EPJ Web Conf. 190 (2018))
We have demonstrated single-photon-sensitive detectors working at 1550 nm with 2 um wire width and area of 360 x 360 um2
Scaling up with “microwires”
J. Chiles et al., SPW 2019
In preparation for submission

## Slide 23: Multilayer target (Stack)
Notes: Next, I’ll talk about the multilayer optical target, or stack. Being a photonics guy, this (and the optomechanical assembly portion) are more where my expertise comes in.

## Slide 24: Multilayer Target
5 pairs of amorphous silicon / silicon dioxide (n = 2.74/1.45)
  λ / 2 thickness stack
    Constructive interference at design wavelength ΛT
    Index contrast of ~ 1.3 at λ = 1550 nm
    Fused SiO2 substrate: minimize thermal expansion mismatch
a-Si
SiO2
Au mirror
…
Notes: The target consists of a 2” diameter fused silicon dioxide wafer, polished on both sides. On the bottom surface, five pairs of amorphous silicon and silicon dioxide have been deposited at lambda/2 optical thicknesses. This, and the gold mirror placed at the bottom, are required for selecting the proper optical mode for maximum signal photon generation. Constructive interference is achieved at a design wavelength I’ll call LambdaT.

## Slide 25: Multilayer target fabrication
Done in-house at NIST
  Highly uniform
  Low-temperature deposition to withstand cryo shock

## Slide 26: Multilayer target characterization
White light interferometry
  Fifth reflectance null after photonic bandgap indicates emission wavelength Λ T
Λ T = 1.55 μm
Λ T = 1.55 μm
Reflectance
Reflectance
Design/Simulation
Experiment/Measured
About 1 dB power loss in optical transmission through the target

## Slide 27: Optomechanical assembly
Notes: The third and final section of my talk will focus on the optomechanical assembly.

## Slide 28: Function of the assembly
Align optical path
  Multilayer target -> Lens -> Detector
  Provide experimental verification
    Laser alignment source for targeting
House detector and electrical interface
Additional light blocking

## Slide 29: Function of the assembly
Align optical path
  Multilayer target -> Lens -> Detector
  Provide experimental verification
    Laser alignment source for targeting
House detector and electrical interface
Additional light blocking
Next: a walkthrough of the assembly and its elements

## Slide 30: Multilayer target, top profile
Alignment aperture
Gold mirror
Target substrate
Multilayer stack
Notes: First we have the target. As we saw before, it’s a silicon dioxide wafer with a multilayer stack, and a gold mirror placed at the end of the multilayers. However, in this profile view, you can see an aperture that we open up in the middle. This is used later for aligning the optical axis to the detector chip.

## Slide 31: Optomechanical assembly
Exploded
Assembled

## Slide 32: First-generation haloscope
Recorded no dark count events in ~26 hours

## Slide 33: Issues identified in pilot run
Challenging to guarantee alignment of signal path to targeting path

## Slide 34: Issues identified in pilot run
Adjustment of lens focal length
  Hugely underfilling the focusing lens leads to large depth of focus (bad)
  Difficult to accurately judge when you’re at focus

## Slide 35: Solutions
Challenging to guarantee alignment of signal path to targeting path
  Co-mount lens, stack and collimator on same optomechanical assembly
  Use collimator with low pointing error off mechanical centerline
Adjustment of lens focal length
  Oversized (1” diameter) reflective collimator
  Invar cage rods for low CTE

## Slide 36
Latest version assembled and ready for detector integration
Target – pre-assembly
1 cm alignment aperture

## Slide 37: Expected reach – run 2
Can break through solar bounds in ~1 day of run time
Notes: Next, I’ll talk about our first experiment using this technology.

## Slide 38: Improving the reach
Detector efficiency improvements
  Currently estimated around 15% (no optimization)
  Can get up to 98% with AR coating and back reflector
    D. Reddy, CLEO 2019, FF1A.3
More layers
  Limited by practical tooling considerations (chamber cleanliness)
  Commercial vendors for thick film sputtering or PECVD
  Need to carefully manage stress, adhesion of films
Longer integration times
  Extended experiment planned soon
Noise mitigation
  Muon veto, optimized detectors, better electrical noise management

## Slide 39: What about muons?
Detector is 400 x 400 um2 with 50% fill factor
   muon flux of 1x10-5 Hz on nanowire active area
Substrate events?
  1x10-2 Hz muon flux across 1x1 cm substrate for chip
  Substrate (Si) does not scintillate
  Detector electrically isolated from Si substrate
Si
SiO2
WSi
WSi

## Slide 40: Measuring muon events
Proposed approach: scintillator “sandwich” with SNSPDs
SNSPD
Si:GaAs chip
Si:GaAs chip
Si chip

## Slide 41
Muon incident on stack:
  Hits first GaAs chip
  Hits Si chip (hits detector)
  Hits second GaAs chip
Light-blocking screens
SNSPDs on GaAs see event due to scattered photons
Veto when Si-SNSPD clicks are coincident with GaAs-SNSPD clicks
~1.3 eV

## Slide 42: Experimental progress on muon veto
Full wafer of SNSPDs on Si:GaAs fabricated
260 x 260 um pixels (1 um wide wires) on 1 cm chips
Integration and testing at MIT soon

## Slide 43: How far can we go?
M. Baryakhtar et al., Phys. Rev. D 98, 035006 (2018)

## Slide 44: Future work
Notes: Before I wrap up, I’ll just touch on a couple exciting directions we are considering taking this approach to dark matter detection.

## Slide 45: Future work: scaling to larger coverage
Experiment scalable by adding multiple targets of different periodicity
  Volume still significant, cryostat volume precious

## Slide 46: Future work: scaling to larger coverage
Experiment scalable by adding multiple targets of different periodicity
  Volume still significant, cryostat volume precious
Modify haloscope design: decouple optics+target from the SNSPD

## Slide 47: Future work: scaling to larger coverage
Can integrate dozens of these in one moderately low-T fridge
  Just cold enough to eliminate blackbody IR coupled into fibers

## Slide 48: Future work: resonant detection schemes
DM can also potentially couple to matter such as molecules
  0.2 – 20 eV sensitivity range
  Many “control knobs” for background rejection

## Slide 49: Future work: resonant detection schemes
DM can also potentially couple to matter such as molecules
  0.2 – 20 eV sensitivity range
  Many “control knobs” for background rejection
Developing suspended target structures for resonant coupling to gases
A. Arvanitaki et al., arXiv:1709.05354 (2017)

## Slide 50
Funding/Support
NIST: Internal funds
MIT: DOE
NIST: Jeff Chiles, Sae Woo Nam, Varun E. Verma, Adriana Lita
MIT: Ilya Charaev, Karl K. Berggren, Marco Colangelo
Perimeter Institute for Theoretical Physics: Asimina Arvanitaki, Junwu Huang
New York University: Masha Baryakhtar
UCSB: Ken Van Tillburg
Stanford: Robert Lasenby
M. Baryakhtar et al., Phys. Rev. D 98, 035006 (2018)
Arvanitaki et al., arXiv:1709.05354 (2017)
Y. Hochberg et al., Phys. Rev. Lett. 123, 151802 (2019)

## Slide 51
Ultimately, SNSPD efficiency can be improved to >98% through well-established techniques
98%
D. Reddy et al, CLEO FF1A.3 (2019)
High system detection efficiency