## Slide 1
Pulse-Shape-Based Analysis using Machine Learning in the Majorana Demonstrator
www.lngs.infn.it
www.sanfordlab.org
www.sanfordlab.org
Laxman Paudel
On behalf of Majorana collaboration
CIPANP 2022

## Slide 2
Outline
Majorana Demonstrator
Traditional Pulse Shape Analysis
Motivation and Network’s Performance:
  Interpretable Machine Learning Model (Part I)
  Pileup Waveforms Study (Part II)
Summary and Outlook

## Slide 3: Majorana Demonstrator
Searching for neutrinoless double-beta decay of 76Ge in HPGe detectors, probing additional physics beyond the standard model, and informing the design of the next-generation LEGEND experiment
Continuing to operate at the Sanford Underground Research Facility with natural detectors for background studies and other physics
Excellent Energy Resolution: 2.5 keV FWHM @ 2039 keV
          and Analysis Threshold: 1 keV
Low Background: 2 modules within a compact graded shield and active muon veto using ultra-clean materials
Reached an exposure of ~65 kg-yr before removal of the enriched detectors for the LEGEND-200 experiment at LNGS
3
Source and Detector: Array of p-type, point contact (PPC) detectors
30kg of 88% enriched 76Ge crystals – 14 kg of natural Ge crystals
Included 6.7 kg of 76Ge inverted coaxial, point contact detectors (ICPC) in final run

## Slide 4
Detector Signal
Falling edge
Rising edge
Baseline
Features of the waveform varies with types of interaction: rising edge carries most of the information
Pulse shape analysis (PSA) parameters are developed to identify the types of interaction
P-type point contact (PPC) geometry enables pulse shape analysis techniques

## Slide 5
Traditional Pulse Shape Analysis
γ
ββ
Multi-site event
Single-site event
Amplitude of current pulse is suppressed for a multi-site event compared to a single-site event of the same event energy (AvsE).
PRC 99 065501 (2019)

## Slide 6: Majorana Demonstrator 2022 Result
Operating in a low background regime and benefiting from excellent energy resolution
Final enriched detector active exposure: 64.5 ± 0.9 kg-yr
Background index at 2039 keV in lowest background configuration
  15.7 ± 1.4 cts/(FWHM t yr)
Frequentist Limit:
  Median T1/2 Sensitivity: 8.1 × 1025 yr (90% C.I.)
  65 kg-yr Exposure Limit: T1/2 > 8.3 × 1025 yr (90% C.I.)
Bayesian Limit: (flat prior on rate)
  65 kg-yr Exposure Limit: T1/2 > 7.0 × 1025 yr (90% C.I.)
Background Index:
  (6.2 ± 0.6) × 10-3 cts/(keV kg yr)
Energy resolution: 2.5 keV FWHM @ Qββ
mββ < 113 - 269 meV
Using M0ν = 2.66 - 6.34
See talk by W. Pettus on Sept 3rd in the plenary session at this meeting for an overview and final results of the Majorana Demonstrator.
Boosted Decision Tree analysis: arXiv:2207.10710

## Slide 7: Rich and Broad Physics Program
PRL 129.081803 (2022)
See talk by C. Wiseman on Aug 30 in Dark Matter session for the Majorana BSM physics.

## Slide 8: Classification with Interpretable Machine Learning Model
Part I
Results are all work in progress

## Slide 9
Motivation for Interpretable Machine Learning
Machine learning based pulse shape analysis has a potential to outperform traditional analysis
We can simultaneously train all detectors to avoid detector by detector tuning
  This will be important for next-generation experiment with a larger channel count like LEGEND
Leverage interpretability to understand the source of the classification power

## Slide 10
Data Selection
228Th calibration data
Signal: DEP events
(single-site)
Background: SEP events
(multi-site)
Data used from 228Th and 56Co calibration data
Collect single escape peak (SEP) and double escape peak (DEP) events based on energy cut
56Co calibration data
Events from 2180 keV DEP peak

## Slide 11
Recurrent Neural Network (RNN)
RNN is a canonical model for processing waveform data – the key improvement here is the inclusion of attention mechanism.
Attention mechanism allows RNN to zoom in the part which contains most important information (rising edge of the waveform)
Attention mechanism also helps to explain the decision of the model
Context vector + final hidden state output
Fully connected NN
Outputs: classification
Attention score is an important tools for interpretability of models
http://colah.github.io

## Slide 12
RNN Training
Waveform in charge domain
Waveform in current domain
Input Features: [waveform, AvsE, detector, start time of the rising edge]
Waveforms are normalized
Training data:
  Multiple detector data with one hot encoding applied to detector ID
  DEP (signal) and SEP (background) events of 2614 keV from 228Th calibration data
  Labeling of waveform (signal label = 1, background label = 0)
Testing data:
  Individual detector data
  DEP at 2180 keV from 56Co data and SEP events at 2103 keV (not seen in training) from 228Th calibration data
Evaluate performance on testing data
Trained model takes 4 features as input and outputs a sigmoid value between [0,1]
Value close to 0 and 1 means the network thinks background-like and signal-like events

## Slide 13: Network Output
Distribution of network outputs for signal-like (DEP) and background-like (SEP) events in the RNN network for a detector.
Charge Domain
Current Domain

## Slide 14: Confusion Matrix
Each entry in a confusion matrix represents classification based on the traditional approach of AvsE and the prediction by the network.
SEP events
DEP events
SEP and DEP events in an example detector:

## Slide 15: SEP Remaining
Lower the percentage of SEP events remaining, better the performance of classification
A good performance of RNN in terms of single-site and multi-site events classification with far less parameters tuning than in AvsE is observed
AvsE has better performance in ICPCs.
ICPC detector

## Slide 16: Interpretability of the Model
Attention score at the rising edge is higher as expected.
Classification power comes from the feature of the rising edge.
Network puts more focus to learn from the rising edge.
Accepted by the model
Rejected by the model
Charge waveform
Charge waveform
Current waveform

## Slide 17: Parameter Regression for Pileup Waveforms
Part II
Results are all work in progress

## Slide 18: Motivation for Pileup Waveform Study
E2
E1
time (ns)
Distinguish between pileup and single waveforms using machine learning approach.
In physics data, there is a small amount of expected pileup waveforms, e.g., the signature of isomeric gamma transition following cosmogenic production of certain isotopes
  Look for shift and energy’s peak ratio (E1/E2) for the signature.
  This determination is implemented as regression in machine learning approach.

## Slide 19: Simulated Pileup Waveforms Dataset
Waveforms are single site events taken from the Calibration data. Use these single waveforms to simulate pileup wfs.
Simulation Parameters:
  Scaling: Random scaling for waveform height for both base (1st) and on-top (2nd) waveform.
  Relative shift (Samples/Bins): Random relative shift for on-top waveform from base waveform.

## Slide 20: RNN Performance for Simulated Pileup Waveforms
GRU
Fully Connected Layer
Good performance for both small and large maximum shifts.
Classification power of RNN to distinguish between single and pileup waveforms
  performs very well when the pileup is obvious.
For shift range of 300 samples

## Slide 21: Parameter Regression in RNN
For real single waveforms (having 0 shift)
For simulated pileup waveforms (having shift between 0 and 100 )
Differences between true shift and predicted shift from the regression is studied
Good parameter determination performance.
Likely boundary effect
  One can filter the waveforms for the pileup first, and then send the pileups for the regression

## Slide 22
Transformer Model
We have some disadvantages of RNN model:
  Lack of long-range correlation
  Sequential processing (therefore can’t be trained in parallel)
Transformer model was first described in 2017 in the paper “Attention is all you need”.
Main characteristics of Transformer model:
    Non-Sequential
    Self Attention
    Positional Embeddings (PE)
It allows parallel computation (to reduce training time), so Transformers are faster than RNN-based models (as all the input is ingested once).

## Slide 23
Parameter Regression in Transformer Model
For simulated pileup waveforms
Shows a similar performance as RNN

## Slide 24
Summary and Outlook
We are developing machine learning tools for various waveform-based analyses in Majorana.
Interpretable RNN models were developed to identify single-site and multi-site events.
  Model was trained using multiple detectors simultaneously and the background rejection is comparable to traditional AvsE parameter with far less tuning, which could be beneficial for experiments with numerous detectors.
  Further study on model interpretability may allow us to learn from the machine to benefit traditional analysis.
Machine learning-based parameter determination expands the scope of ML applications.
  Reasonable determination of the time shift parameter in pile-up waveforms.
  We have some success on multidimension regression in extracting both the shift and energy’s peak ratio simultaneously.
  This could be used to look for the signature of isomeric gamma transition in real data.
Machine learning-based tools can be valuable for the next-generation Ge-based project, LEGEND.
This material is supported by the U.S. Department of Energy, Office of Science, Office of Nuclear Physics, the Particle Astrophysics and Nuclear Physics Programs of the National Science Foundation, and the Sanford Underground Research Facility.
Boosted Decision Tree for Majorana, arXiv:2207.10710
Final result from Majorana, arXiv:2207.07638
Majorana and LEGEND talks at this conference:
W. Pettus,
Final results from the
Majorana Demonstrator,
Plenary session, Sept. 3rd
C. Wisemen
Exotic dark matter searches with the Majorana Demonstrator
DM session Aug. 30th
C.J. Barton
An update on muon-induced backgrounds in LEGEND-1000
Nu session Aug. 30th
W. Xu
The search of neutrinoless double beta decay and the LEGEND experiment
NN session Sept. 3rd

## Slide 26
Backup Slides

## Slide 27: Quantitative Analysis
ROC (Receiver operating characteristic) curve
True positive Rate
False positive Rate
ROC-AUC (Area under ROC curve) value is a measure of classification power!
Smaller SEP remaining for same acceptance of TPR is better!

## Slide 28: Waveforms Rejected by RNN but Accepted by AvsE

## Slide 29: Multilabel Regression (Initial Result)
Waveform dataset has shift (< 500 samples) and E_ratio (<100)

## Slide 30: CNN Output for Pile-up and No Pile-up Waveforms:
CNN outputs for a maximum shift range up to 5 samples (50 ns) and a maximum shift range up to 300 samples (3000 ns).
  Clear identification achieved in both cases

## Slide 31: AUC Value as a Function of Maximum Shifts in Separate Simulations:
Maximum
Good performance for large maximum shifts
Unstable performance for small maximum shifts
AUC Value as a Function of Maximum Shifts in Separate Simulations: