## Slide 1
Traineeships in Advanced Computing for High Energy Physics (TAC-HEP)
Varun Sharma
University of Wisconsin – Madison, USA
GPU & FPGA module training: Part-2
Week-4: Vivado HLS: Pragma’s effect on performance
Lecture-8: April 12th 2023

## Slide 2: So Far…
FPGA and its architecture
  Registor/Flip-Flops, LUTs/Logic Cells, DSP, BRAMs
  Clock Frequency, Latency
  Extracting control logic & Implementing I/O ports
Parallelism in FPGA
  Scheduling, Pipelining, DataFlow
Vivado HLS
  Introduction, Setup, Hands-on for GUI/CLI, Introduction to Pragmas
Today:
Continue with Pragmas and their effects on performance

## Slide 3: HLS Pragmas Effect [Ref]
Performance in term of Resource utilization and timing (latency)

## Slide 4: Pragmas by type
Type | Attributes | 
Kernel Optimization | pragma HLS allocation pragma HLS expression_balance pragma HLS latency | pragma HLS reset pragma HLS resource pragma HLS stable
Function Inlining | pragma HLS inline pragma HLS function_instantiate | 
Interface Synthesis | pragma HLS interface | 
Task-level Pipeline | pragma HLS dataflow pragma HLS stream | 
Pipeline | pragma HLS pipeline pragma HLS occurrence | 
Loop Unrolling | pragma HLS unroll pragma HLS dependence | 
Loop Optimization | pragma HLS loop_flatten pragma HLS loop_merge | pragma HLS loop_tripcount
Array Optimization | pragma HLS array_map pragma HLS array_partition | pragma HLS array_reshape
Structure Packing | pragma HLS data_pack | 

## Slide 5: Pragma HLS allocation
Instance<list>*: Name of the function, operator, or cores
limit=<value>*: Specifies the limit of instances to be used in kernel
<type>*: Specifies the allocation applies to a function, an operator or a core (hardware component) used to create the design (such as adder, multiplier, BRAM)
  Function: allocation applies to the functions listed in the instances=
  Operation: applies to the operations listed in the instances=
  Core: applies to the cores
#pragma HLS allocation instances=<list> limit=<value> <type>
Kernel Optimization

## Slide 6: Example

## Slide 7: Pragma HLS allocation
WITHOUT PRAGMA
WITH PRAGMA
#pragma HLS allocation instances=<list> limit=<value> <type>

## Slide 8: Pragma HLS allocation
#pragma HLS allocation instances=<list> limit=<value> <type>
WITHOUT PRAGMA
WITH PRAGMA

## Slide 9: Pragma HLS Latency
HLS always tries to minimize latency in the design
When LATENCY pragma is specified
  Min < Latency < Max: Constraint is satisfied, No further optimization
  Latency < min: It extends latency to the specified value, potentially increasing sharing
  Latency > max: Increases effort to achieve the constraints
    Still unsuccessful: issue a warning & produce design with the smallest achievable latency in excess of maximum
#pragma HLS latency min=<int> max=<int>
Kernel Optimization

## Slide 10: Pragma HLS Latency
#pragma HLS latency min=4

## Slide 11: Pragma HLS Latency
#pragma HLS latency min=4
WITHOUT HLS Latency PRAGMA
WITH HLS Latency PRAGMA

## Slide 12: Pragma HLS Latency
Not much change in the resources
WITHOUT HLS Latency PRAGMA
WITH HLS Latency PRAGMA
#pragma HLS latency min=4

## Slide 13: Pragma HLS Dataflow
Enables task-level pipelining: allow functions and loops to overlap in their operation
  Increases the concurrency of the RTL implementation & thus the overall throughput of the design
In the absence of any directives that limit resources (like pragma HLS allocation), HLS seeks to minimize latency & improve concurrency
  Data dependencies can limit this, hence proper dataflow is needed
Task-level pipeline
#pragma HLS dataflow
Without DATAFLOW pipelining
With DATAFLOW pipelining

## Slide 14: Pragma HLS Dataflow
#pragma HLS dataflow

## Slide 15: Pragma HLS Dataflow
Without DATAFLOW pipelining
With DATAFLOW pipelining
#pragma HLS dataflow

## Slide 16: Pragma HLS Dataflow
Without DATAFLOW pipelining
With DATAFLOW pipelining
#pragma HLS dataflow

## Slide 17: Pragma HLS Dataflow
Without DATAFLOW pipelining
With DATAFLOW pipelining
#pragma HLS dataflow

## Slide 18: Pragma HLS Inline
Removes a function as a separate entity in the hierarchy
The function is dissolved into the calling function and no longer appears as a separate level of hierarchy in RTL design
May improve area by allowing the components within the function to be better shared or optimized with the logic in the calling function
#pragma HLS inline <region | recursive | off>
Region: Optionally, all functions (sub-functions) in the specified region are to be inlined
Recursive: Inlines all functions recursively within the specified function or region
  By default, only one level of function inlining is performed
Off: Disables function inlining to prevent specified functions from being inlined
  For example, HLS automatically inlines small functions & with the off option, automatic inlining can be prevented
Function inlining

## Slide 19: Pragma HLS Inline
#pragma HLS inline

## Slide 20: Pragma HLS Inline
With HLS INLINE
With HLS INLINE OFF
#pragma HLS inline off

## Slide 21: Pragma HLS Inline
With HLS INLINE
With HLS INLINE OFF
#pragma HLS inline off

## Slide 22: Pragma HLS Inline
No change in the execution order
With HLS INLINE
With HLS INLINE OFF
#pragma HLS inline off

## Slide 23: Pragma HLS Pipeline
The PIPELINE pragma reduces the II for a function or loop by allowing the concurrent execution of operations
A pipelined function or loop can process new inputs every <N> clock cycles
If HLS can’t create a design with the specified II, it issues a warning and creates a design with the lowest possible II
Without Loop pipelining
With Loop pipelining
#pragma HLS pipeline II=<int>
Pipelining

## Slide 24: Pragma HLS Pipeline
#pragma HLS pipeline II=2
With HLS PIPELINE II=2
With DATAFLOW pipelining

## Slide 25: Pragma HLS Pipeline
With HLS PIPELINE II=2
With DATAFLOW pipelining
#pragma HLS pipeline II=2

## Slide 26: Pragma HLS Pipeline
With HLS PIPELINE II=2
With DATAFLOW pipelining
#pragma HLS pipeline II=2

## Slide 27: Pragma HLS Pipeline
#pragma HLS pipeline II=2
With HLS PIPELINE II=2
With DATAFLOW pipelining

## Slide 28: Pragma HLS unroll
Unroll loops to create multiple independent operations rather than a single collection of operations
UNROLL pragma transforms loops by creating multiples copies of the loop body in the RTL design, which allows some or all loop iterations to occur in parallel
Loops in the C/C++ functions are kept rolled by default
  When loops are rolled, synthesis creates the logic for one iteration of the loop, and the RTL design executes this logic for each iteration of the loop in sequence
UNROLL pragma allows the loop to be fully or partially unrolled
  Fully unrolling the loop creates a copy of the loop body in the RTL for each loop iteration, so the entire loop can be run concurrently
  Partially unrolling a loop lets you specify a factor N
#pragma HLS unroll

## Slide 29: Pragma HLS unroll
#pragma HLS unroll

## Slide 30: Pragma HLS unroll
#pragma HLS unroll
Without UNROLL For-loop
With UNROLL For-loop

## Slide 31: Pragma HLS unroll
#pragma HLS unroll
Without UNROLL For-loop
With UNROLL For-loop

## Slide 32: Pragma HLS array_partition
Array optimization
Figure
Cyclic: Cyclic partitioning creates smaller arrays by interleaving elements from the original array
Block: Block partitioning creates smaller arrays from consecutive N-blocks of the original array
Complete: Complete partitioning decomposes the array into individual elements
  For a 1-D array, this corresponds to resolving a memory into individual registers (default <type>)
#pragma HLS array_partition variable=<name> <type> factor=<int> dim=<int>

## Slide 33: Pragma HLS array_partition
#pragma HLS array_partition variable=<name> <type> factor=<int> dim=<int>

## Slide 34: Pragma HLS array_partition
#pragma HLS array_partition variable=<name> <type> factor=<int> dim=<int>
Without Array partitioning
With Array Partitioning

## Slide 35: Pragma HLS array_partition
#pragma HLS array_partition variable=<name> <type> factor=<int> dim=<int>
Without Array partitioning
With Array Partitioning

## Slide 36: Pragma HLS array_partition
#pragma HLS array_partition variable=<name> <type> factor=<int> dim=<int>
Without Array partitioning
With Array Partitioning

## Slide 37: Combination of Pragmas
ARRAY Partitioning + UNROLLING For loop

## Slide 38: For loop unrolling + Array Partitioning
#pragma HLS ARRAY_PARTITION variable=in complete dim=1
#pragma HLS ARRAY_PARTITION variable=out complete dim=1
#pragma HLS unroll

## Slide 39: For loop unrolling + Array Partitioning
Without Pragma
With Pragmas

## Slide 40: For loop unrolling + Array Partitioning
Without Pragma
With Pragmas
Is it a good optimization?

## Slide 41: Summary
Pragmas are important to implement a design in best possible ways
There are a lot of pragmas to help the design implementation
Be careful with the choice of pragma’s to avoid conflicts
Different pragma’s help improve different aspects of design or performance parameters

## Slide 42: Assignment Week-4
Do a matrix multiplication of two 1-dimensional arrays – A[N]*B[N], where N > 5
  Report synthesis results without any pragma directives
  Add as many pragma directives possible
    Report any conflicts (if reported in logs) between two pragmas
Compare the analysis perspective (Performance) for different case shared today
For Array_partitioning, instead of using complete, use block and cyclic with different factors

## Slide 43: Questions?

## Slide 44: Acknowledgement
Lectures are compiled using content from Xilinx’s public pages or different user guides

## Slide 45: Additional material

## Slide 46: Assignment submission
Where to submit:
  https://pages.hep.wisc.edu/~varuns/assignments/TAC-HEP/
Use your login machine credentials
Submit one file per week
Try to submit by following week’s Tuesday

## Slide 47: Correct Time
  From 03.28.2023 onwards
  Tuesdays: 9:00-10:00 CT / 10:00-11:00 ET / 16:00-17:00 CET
  Wednesday: 11:00-12:00 CT / 12:00-13:00 ET / 18:00-19:00 CET

## Slide 48: Jargons
ICs - Integrated chip: assembly of hundreds of millions of transistors on a minor chip
PCB: Printed Circuit Board
LUT - Look Up Table aka ‘logic’ - generic functions on small bitwidth inputs. Combine many to build the algorithm
FF - Flip Flops - control the flow of data with the clock pulse. Used to build the pipeline and achieve high throughput
DSP - Digital Signal Processor - performs multiplication and other arithmetic in the FPGA
BRAM - Block RAM - hardened RAM resource. More efficient memories than using LUTs for more than a few elements
PCIe or PCI-E - Peripheral Component Interconnect Express: is a serial expansion bus standard for connecting a computer to one or more peripheral devices
InfiniBand is a computer networking communications standard used in high-performance computing that features very high throughput and very low latency
HLS - High Level Synthesis - compiler for C, C++, SystemC into FPGA IP cores
DRCs - Design Rule Checks
HDL - Hardware Description Language - low level language for describing circuits
RTL - Register Transfer Level - the very low level description of the function and connection of logic gates
FIFO – First In First Out memory
Latency - time between starting processing and receiving the result
  Measured in clock cycles or seconds
II - Initiation Interval - time from accepting first input to accepting next input

## Slide 49: Reminder: Steps to follow
Step-1: Creating a New Project/Opening an existing project
Step-2: Validating the C-source code
Step-3: High Level Synthesis
Step-4: RTL Verification
Step-5: IP Creation

## Slide 50: Assignment Week-3
Use target device: xc7k160tfbg484-2
Clock period of 10ns
1. Execute the code (lec5Ex2.tcl) using CLI (slide-25) and compare the results with GUI results for C-Simulation, C-Synthesis
2. Vary following parameters for two cases: high and very high values and compare with 1 for both CLI and GUI
  Variable: “samples”
  Variable: “N”
3. Run example lec3Ex2a