## Slide 1: Foucault Pendulum
To develop an ongoing, interactive experiment to demonstrate the Earth’s rotation.
Thus far, basic testing and construction of the Foucault Pendulum have been done. The top assembly has been completed, and the pendulum bob has been attached to the wire. Tests measuring the pendulum’s precession frequency and damping speed have been roughly accomplished.
There is more testing that must be done. Also, an excitation and damping mechanism must be developed to run the pendulum continuously.

## Slide 2: Vital Facts and Activities
Peter Weix, Professor Carlsmith, and I have constructed the basic components of the pendulum.
Conducted tests aiming to discover the precession frequency and the damping time.
Discussed future opportunities for the pendulum with Professor Cary Forest, Professor Carlsmith, Professor Demski and Peter Weix.

## Slide 3: Results/Accomplishments/Progress
Chart: Damping time for the Foucault Pendulum
| 0 | 15 | 30 | 45 | 60
 | 1.756 | 1.508 | 1.33 | 1.189 | 1.062
Observed Period = 9.677±.08 seconds
Length = 22.86 meters
Gravity of Earth ≈ 9.81 meters/second^2
Calculated period ≈ 9.591 seconds
Observed Precession Frequency per hour = 7.75°
Calculated Precession Frequency per hour = 10.24°
The damping time for the pendulum is significant. Within a hour the amplitude had decreased by more than half a meter.

## Slide 4: Issues and Needs
Flexing of the Roof
  1” steel plate
Damping
  Excitation mechanism
Elliptical Motion
  Charon ring

## Slide 5: Action Items and Plans
Accomplish another round of testing with what we have now.
Construct a smaller scale Foucault pendulum for which the excitation and damping mechanisms can be tested on.
Begin creating an electromagnetic excitation mechanism that will allow the pendulum to run continuously.
Create or purchase a Charon ring that can damp the radial motion of the pendulum.