## Slide 1: Brain Computer Interfaces: Digital Signal Processing of Steady-State Visually Evoked Potentials
Ian Linsmeier & Ahmed Saif
ECE630

## Slide 2: Brain Computer Interface (BCI)
Vialatte et al. Prog Neurobiol. 2010, 90(4).
Notes: Typical User Interface – physical inputs transduced into digital signals to interpret user intention
BCI – Electrical activity in the brain is transduced into digital signals to interpret user intention. There is no physical input required for BCIs.
Typical Interface with electronics:
Peripheral hardware device
User performs a physical action on the peripheral hardware
The physical action is transduced by hardware device and converted to a digital input
The digital input is interpreted by the computer and, if valid, executes the command
The computer will give the user visual feedback
EX: User physically moves mouse to direct the onscreen cursor. The user clicks an onscreen object, such as an desktop application shortcut, and the computer opens the selected application.
Brain-Computer Interface:
No peripheral hardware for the user to interact with
Instead, BCI measures the electrical activity within the users brain (EEG)
BCI is programmed to recognize certain brain activation patterns
BCI is preprogrammed or learns to associate certain activation patterns with an executable command
When the BCI recognizes a particular activation pattern, it executes the associated command
Again, visual feedback is provided to the user to confirm the correctly executed command
Therefore, the user can make decisions modulating their thoughts, such as thinking of particular idea or action
Conversely, systems can be designed to stimulate electrical activity within the user’s brain – in this case the activated pattern has particular characteristics that are conserved from person to person and can be measure relaibly

## Slide 3: Dependent vs Independent BCIs
Dependent BCI – System is dependent upon a minimal level of neuromuscular control by the user
Independent BCI – System is independent of neuromuscular control by the user (not necessary)
Notes: The most commonly used dependent BCI measures steady state visually evoked potentials.
Dependent
  Ex: Gazing at a particular flashing number on the screen of many numbers
Independent
  Ex: The user thinks of the number and the system can recognize the thought pattern.

## Slide 4: Steady State Visually Evoked Potential-Brain Computer Interface (SSVEP-BCI) System Overview

## Slide 5: Repetitive Visual Stimulus (RVS)
Vialatte et al. Prog Neurobiol. 2010, 90(4).
Flickering LED
(Simple Flicker)
Notes: RVS = stimulatory patterns
Complex RVS = rapidly changing visual pattern
  Higher SNR ratio
Simple RVS = flashing light or simple graphic
  Easier to implement
  Can utilize more of them
RVS fundamental frequency induces SSVEP with same fundamental frequency
Each RVS correspond to a single user option
  The more RVS’s in a system the more user options that are available to the user

## Slide 6: Steady State Visually Evoked Potential (SSVEP)
Vialatte et al. Prog Neurobiol. 2010, 90(4).
RVS frequency→ 10Hz
SSVEP → 10Hz
Notes: Most common signal measured by dependent-BCIs. Measured with EEG
Steady State visually evoked potentials can be reliably induced and measured in the visual cortex of a user’s brain
SSVEPs are stimulated by exposing the user to one (or more) repetitive visual stimuli (discussed next), which are the stimulatory patterns that I mentioned previously.
These patterns will flash at a particular frequency to induce an SSVEP in the brain at that same fundamental frequency.

## Slide 7: SSVEP-BCI System Components
Vialatte et al. Prog Neurobiol. 2010, 90(4).
Notes: User focuses gaze on a particular repetitive visual stimulus, such as a flickering checkerboard pattern. Each repetitive visual stimulus will induce steady state visually evoked potential in the user’s brain with the same fundamental frequency as the excitatory RVS. An EEG measures the brain signals in real time and relays these signals to the computer for SSVEP detection and classification. By matching the SSVEP signals to their excitatory repetitive visual stimulus, the BCI system can infer the user’s intentions.
How do BCI systems work?
In the Diagram above, the user has two options: she can toggle a switch on or off
Certain BCIs are able to interpret her intention simply by recognizing the brain activation patterns that she associates with the concept of “on” or “off”
In the above case, however, the user focuses on one of the two patterns on the screen. Each pattern is associated with one of the two options, and when she focuses on one of the patterns, it will stimulate a brain signal unique to that pattern. Therefore, she can convey her intentions to the BCI system by gazing at a particular pattern.
These brain activation patterns are measured in real time by a measurement device, usually an EEG
The EEG recordings are transferred to the computer system for analysis
The computer is programmed to identify certain brain signals and associate them with user intention.
In the above case, the user focuses on the pattern associated with “on”, which induces a signal in the user’s brain with the same characteristics as the stimulatory pattern
The computer in this system is programmed to recognize the stimulated signal and match it with the one of the possible user options
Through this process, the system can infer the intention of the user without any physical input
User – brain provides the signal that drives the whole system
Measurement Device – measures electrical activity in the brain
  EEG
Computer system – detects, extracts, and analyzes certain activation patterns within the brain
  Recognition of preprogrammed or learned patterns communicates the user’s intention to the computer
  Translates brain activation patterns into user intention by associating the recognized brain pattern with its corresponding command
  Computer executes command or communicates (moving a computer cursor on screen) with additional hardware
Additional Hardware – Often the computer will communicate with another piece of hardware (such as a motorized wheelchair or a drone) to relay their intentions to the terminal device.
Graphical display that communicates feedback to the user

## Slide 8: Designing a SSVEP-BCI System

## Slide 9: SSVEP-BCI Design Parameters
Repetitive Visual Stimuli
Brain Signal Measurement
SSVEP Detection
SSVEP Classification
Vialatte et al. Prog Neurobiol. 2010, 90(4).
1
2
3 & 4
Notes: Our components effectively become our design parameters when engineering an SSVEP

## Slide 10: RVS Design
1 RVS = 1 User Option
Number of RVS’s
Simple vs. Complex
Frequency Range
  3.5 to 75 Hz
  15 Hz is optimal
Vialatte et al. Prog Neurobiol. 2010, 90(4).
Notes: Simple vs. complex
  Complex = higher SNR
  Simple = can incorporate many more
Number of RVS’s = number of user options
Frequency Range
  Want freqs near 15Hz, retina has highest SNR in this region
  Avoid freqs over 30Hz because they are subject to electromyographic (muscle activity) interference
  Choose well resolved frequencies (sufficiently spaced apart so its easier to detect and identify the frequency)
  Do not choose frequencies that are higher harmonics of other RVS frequencies
    (RVS at 7 Hz, do not choose RVS at 14Hz as another RVS)

## Slide 11: Measuring SSVEP
Itai et al. EMBC Annual International Conference. 2012.
Measurement Location
  Visual Cortex
Number of electrodes
  1 or 2 is usually sufficient
Notes: EEG Electrodes
Measurement Location
  Over the visual cortex of the brain (near the inion region)
Number of electrodes used
  Usually 1-2 electrodes is sufficient
  Can use more electrodes for sophisticated SSVEP-BCI Systems
SSVEPs contain energy at their fundamental frequency (ff RVS) as well as their higher harmoincs
  The largest amount of the energy is often contained at the fundamental frequency

## Slide 12: Two General BCI Paradigms
Small number of user options (≤4)
  Usually employ Complex RVS’s due to higher SNR
Large number of user options (>4)
  Usually employ simple RVS’s
Notes: Most SSVEP BCI’s use an EEG and take measurements from one or multiple electrodes over the visual cortex (this doesn’t really change the paradigm that one is operating in for SSVEP BCI’s)
However the type and number of RVS’s employed does determine the paradigm of the BCI system, and can be broken down into two general categories:
Paradigm 1:
BCI Systems in this paradigm employ complex RVS’s, which limits the number of total RVS’s that can be feasibly employed to a max of 4. However, since the system uses complex RVS, the SSVEP signals induced in the user’s brain will have a significantly higher SNR and will thus be easier to detect.
Paradigm 2:
BCI systems in the paradigm can employ any number of user options and are often used when one wants to incorporate 5 or more user options into the system. For these systems, simple RVS’s, such as blinking LEDs, are used because they are easy to implement and array. These LEDs invoke SSVEPs with lower SNRs making them harder to detect
These two paradigms can be further broken down based upon the Digital signal processing framework used to detect and identify measured SSVEPs

## Slide 13: SSVEP Detection Methods
Power Spectral Density (PSD) Analysis
  Nonparameteric Methods (Fourier Analysis)
  Parametric Methods (AR Modeling)
Canonical Correlation Analysis (CCA)
Continuous Wavelet Transform (CWT)
Notes: Although choosing the appropriate hardware configuration is important when designing SSVEP-BCI systems for certain applications, the performance of a SSVEP-BCIs in either paradigm is primarily dictated by the methods used to perform SSVEP detection. In general, the detection methods take the acquired EEG signals, eliminate noise, extract SSVEP features, and classify the SSVEP using a priori knowledge of the RVS fundamental frequencies. Depending on the application of the system, only certain detection methods will be able to rapidly and accurately identify and match SSVEP signals to their corresponding excitatory RVS. Therefore, the choice of SSVEP detection method may be the most important determinant of a successful SSVEP-BCI system.
For the remainder of this presentation we will discuss different
The DSP method used for SSVEP analysis is probably the most important design choice for an engineer designing a SSVEP BCI system.
Certain SSVEP BCI applications would not be possible if the correct detection method isn’t used; therefore, the optimal choice of detection method for any SSVEP-BCI is critical when designing such as system.
Here we will discuss the 3 (or four) most common DSP methods used to detect SSVEP, including:
Both nonparametric and parametric power spectral density analysis
Canonical Correlation Analysis
Continuous Wavelet transform

## Slide 14: Nonparametric PSD Analysis
Bin et al. J. Neural Eng. 2009, 6(4).
Notes: Since SSVEPs are periodic, the power spectral density can be used to detect them amongst random EEG signals
Use autocorrelation function of the signal to calculate the power spectral density.
Converts from time domain to an energy distribution in the frequency domain
Can’t perform this calculation in practice.
Must use estimators:
1.) Averaged Periodogram
2.) AR Modeling

## Slide 15: Periodogram Estimates PSD
(Asymptotically Unbiased as L → ∞)
(Not a consistent estimator)

## Slide 16: Averaged Periodogram
Break down signal into intervals of fixed length and average each interval together
No Averaging → 10 Interval Average → 20 Interval Average
Vialatte et al. Prog Neurobiol. 2010, 90(4).
Notes: Decreases Variance of the signal at the cost of resolution.
This is fine for SSVEP signal detection since the resolution between the signals is determined by our choice of RVS fundamental frequencies

## Slide 17: Parametric PSD Analysis
Parametric Models:
  Moving Average (MA) – All Zeros
  Autoregressive (AR) – All Pole
  Autoregressive Moving Average (ARMA) – Poles and Zeros
Smondrk et al. IEEE. 2013.
Notes: We know that the output power spectrum for an LTI system is product of the input power spectrum and the magnitude squared of the frequency response for the LTI system. Since the power spectrum for white noise is constant, we can represent various spectra by altering the frequency response of the LTI system; this can be performed by iteratively adjusting the model parameters until the output of the LTI system describes the random signal of interest.

## Slide 18: AR Modeling of SSVEP Signals
Caclulate ak coefficients using the Yule Walker Equations:
http://paulbourke.net/miscellaneous/ar/
Notes: Use the AR Model to match signals behavior as closely as possible
We can achieve increased resolution using AR models as compared to the nonparametric methods.
Additionally, a much smaller signal length can be used to generate a PSD estimate of the signal.
However, AR modeling suffers from incorrect model approximations that can lead to large deviations from the signals true behavior.

## Slide 19: Canonical Correlation Analysis (CCA)
Lin et al. IEEE Trans. Biomed. Eng. 2007, 54(6)

## Slide 20: Continuous Wavelet Transform (CWT)
Wavelets can localize a signal in both frequency and time
Acts like a short time Fourier transformation but with varying window sizes based on frequency
With the correct mother wavelet we can achieve a result better than the FFT and PSD

## Slide 21: SSVEP Classification
Yeh et al. Biomed Eng Online. 2013, 12(46)
Notes: Chia-Lung Yeh, Po-Lei Lee, Wei-Ming Chen, Chun-Yen Chang, Yu-Te Wu and Gong-Yau Lan.
BioMedical Engineering OnLine Volume 12, http://www.biomedical-engineeringonline.com/content/12/1/46

## Slide 22: Support Vector Machine (SVM)
http://en.wikipedia.org/wiki/File:Svm_separating_hyperplanes_(SVG).svg
Notes: Graphic showing how a support vector machine would choose a separating hyperplane for two classes of points in 2D. H1 does not separate the classes. H2 does, but only with a small margin. H3separates them with the maximum margin

## Slide 23: A Comparison of SSVEP Detection Methods

## Slide 24: Comparison of SSVEP Detection Methods
Method | The average time of calculation [ms]
PSD | 1.8 ± 0.1
PSDw | 1.1 ± 0.1
AR | 13.7 ± 0.6
ARw | 10.2 ± 0.4
CCA | 52.6 ± 0.7
CWT | 114.2 ± 2.8
Smondrk et al. IEEE. 2013.
Notes: M. Smondrk, M. Vozda, J. Krohova, B. Hrvolova, T. Peterek, and M. Penhaker, “A comparison of success and time consumption of the most common methods for detection of the SSVEP,” in 2013 36th International Conference on Telecommunications and Signal Processing (TSP), 2013, pp. 657–661.

## Slide 25: Comparison of SSVEP Detection Methods
Smondrk et al. IEEE. 2013.
Notes: Smondrk et al. IEEE. 2013.

## Slide 26: SSVEP Detection for BCI Paradigms
Paradigm 1: Systems will small number of user options (≤4 options)
  Employ Complex RVS’s (checkerboard)
  Nonparametric PSD using well resolved RVS’s
Paradigm 2: Systems using large number of user options (>4 options)
  Employ Simple RVS’s (LEDs)
  Canonical Correlation Analysis

## Slide 27: Questions?